## Slide 1: Assessment of the Extra Capacity Required of Alternative Energy Electrical Power Systems to Completely Replace Fossil Fuels
Simon P. Michaux
18/08/2022
Associate Professor Mineral Processing & Geometallurgy

## Slide 2: The industry changed in 2005
A case can be made that this blow out was a chain reaction started in the oil industry
The change started something like 17 years in our past
A major economic correction (GFC 2008) did not resolve the problems

## Slide 3: Summary
Link to full report below
https://tupa.gtk.fi/raportti/arkisto/42_2021.pdf
Link to 8 page summary
https://mcusercontent.com/72459de8ffe7657f347608c49/files/be87ecb0-46b0-9c31-886a-6202ba5a9b63/Assessment_to_phase_out_fossil_fuels_Summary.pdf
Using same energy mix as 2018, determine how many new non-fossil fuel power stations are needed
Physical Tasks done industrially by fossil fuels
Determine the true scope of useful work done
Assemble non-fossil fuel systems that could do the same useful work
Calculate the quantity of electrical power needed
Number of vehicles, by class
Number and size of batteries
An understanding of the EV to H2-Cell split
Estimates of EV & H2-Cell rail transport
Estimates of an EV & H2-Cell maritime shipping fleet
Estimates of phasing out of fossil fuel industrial applications
Examination of the feasibility of expanding the nuclear NPP fleet
Assessment of the feasibility of global scale biofuels
Plastics & fertilizer industries

## Slide 4: What would it take to replace the existing fossil fuel system?
Phase out fossil fuels & non-fossil fuel systems implemented
Economic growth once new system is stable
Existing system is fully replaced
(2018 scope used)
What is the true scope of tasks to fully phase out fossil fuels, and the complete replacement with non-fossil fuel powered systems?
Existing ICE transport fleet size
  Cars & Trucks
  Rail
  Maritime shipping
  Aviation
What is the number and size of required batteries/hydrogen cells/solar panels/wind turbines
  In 2018, 84.5% of global primary energy consumption was fossil fuel based
Required power grid expansion to charge the needed number of batteries, and make hydrogen
  Number of new power stations
  Required power storage to manage intermittent supply
Current plans are not large enough in scope, the task before us is much larger than the current paradigm allows for

## Slide 5: Baseline calculation
The global fleet of vehicles is estimated to be 1.416 billion, which travelled an estimated 15.87 trillion km in the year 2018
  0.7% is EV in 2020
For the same energy output:
  …an Electric Vehicle system requires battery storage mass 3.2 times the fuel tank (@700bar) mass of a hydrogen H-Cell system
  …meanwhile a hydrogen H-Cell system will require 2.5 times more electricity compared to a Electric Vehicle system
All short-range transport could be done by Electric Vehicle systems
  All passenger cars, commercial vans, delivery trucks and buses (1.39 billion vehicles), would travel 14.25 trillion km in 365 days
  This would require 65.19 TWh of batteries (282.6 million tonnes of Li-Ion batteries)
All long-range distance transport could be powered with a hydrogen fuel cells
  All Class 8 HCV trucks, the rail transport network (including freight), and the maritime ship fleet
  In total, 200.1 million tonnes of hydrogen would be needed annually

## Slide 6
62 million Motorcycles 160 billion km
29 million Buses & Delivery Trucks 803 billion km
695.2 million Passenger Cars 5.4 trillion km
1 128.5 TWh
1 166.1 TWh
19.4 billion kWh
601 million Vans, Light Trucks 7.9 trillion km
2 181.7 TWh
1.39 billion Electric Vehicles
Charging Batteries
GLOBAL SYSTEM I
Building Heating
Steel Manufacture
Electrical Power Generation
17 086.1 TWh
2 816.0 TWh
56.5 TWh
Industry
4 495.7* TWh
19 958.6 TWh
*updates in EV energy efficiency reduced this number by 4% from (Michaux 2021)

## Slide 7
28.9 million Class 8 HCV Trucks
Travelled 1.62 trillion km
129.9
million tonnes
Maritime Shipping cargo
72 146 billion tonne-km
51.7
million tonnes
18.5
million tonnes
Rail Transport 9 407 billion tkm freight
1 720 billion passenger-kilometers
7 503.7 TWh
1 066.5 TWh
2 983.4TWh
Hydrogen
H2-Cell Vehicles
Manufacture of H2
200.1 million tonnes
Hydrogen Economy
Aviation
Plastics Manufacture
Biofuel ??? liters
Biomass Sustainably Sourced from the Planetary Environment
Biomass Feedstock ??? tonnes
Biomass Economy
11 553.6 TWh
GLOBAL SYSTEM II
Sustainability audit

## Slide 8
GLOBAL SYSTEM III
=
586 032 NEW Non-Fossil Fuel Power Stations
EV 4 495.7 TWh
Industry 19 958.6 TWh
H2 11 553.6 TWh
Additional Annual Electrical Power Requires 36 007.9 TWh
Wind Power
13 800.4 TWh
169 867 stations
Solar Power
13 800.4 TWh
393 840 stations
Nuclear Power
2 701.4 TWh
211 stations
4 809.6 TWh
3 628 stations
Hydro Power
Other Renewables
Geothermal & Tidal
266.7 TWh
442 stations
Biowaste to Energy
624.0 TWh
18 044 stations
Power storage buffer 548.9 TWh
Power plant fleet in 2018 was 46 423 stations

## Slide 9
Global total power generation and the installed capacity of power generation sources in 1.5°C Scenario in 2018, 2030 and 2050 (Source: IRENA 2022)

## Slide 10: To deliver 1000 TWh of power to the grid over 1 year…
Renewables have a much lower ERoEI ratio than fossil fuels and may not be strong enough to power the next industrial era
(Source Data: Global Energy Observatory, Agora Energiewende and Sandbag 2019)

## Slide 11
Electrical power required to phase out gas and coal power generation
Electrical power required charge EV batteries
Electric power required to produce hydrogen for H2-Cell vehicles
Electrical power required to phase out gas building heating
Electrical power required to phase out coal fired steel manufacture
Coal
Gas
Oil
Extra electrical power annual capacity required to be installed
17 086.1 TWh to be phased out
9 528.7 TWh
Existing Non-fossil Fuel Power Generation
36 007.9 TWh
Total electrical power production in 2018 was 26 614 TWh
2nd generation of work done

## Slide 12: New energy split
695.2 million passenger cars (EV)
46.8 kWh battery
29 million buses (EV)
227.5 kWh battery
601.3 million commercial vans (EV)
42 kWh battery
62 million motorcycles (EV)
12 kWh battery
28.9 million trucks (H2-Cell)
4 495.7 TWh
19 958.6 TWh
Electrical Power Generation, heating & steel manufacture
11 553.6 TWh
36 007.9 TWh
New annual capacity
36 007.9 TWh
New annual capacity
Developed from a combination of an IEA 2021 projection and some of my own assumptions

## Slide 13: Gas and hydro are the existing buffer

## Slide 14
Distribution of the sun’s radiation energy over the year in Germany (Wesselak & Voswinckel 2016)

## Slide 15: Wind is highly variable
Reliable capacity as a % of max capacity for wind 7-25% (UK Parliament 2014)
  Power production was so erratic it could not be predicted
Variations in power produced can last weeks and, in some cases, months
In practical terms, global power generation operating hours in 2018 (Global Energy Observatory)
  Solar PV produced 11.4% of the calendar year
  Wind produced 24.9% of the calendar year
Highly variable of when power was produced

## Slide 16: Power supply & demand
Transport demand could function on a 48-hour buffer
Wind & solar electrical power production could need a buffer of several months if they make up a large portion of the energy mix
https://www.youtube.com/watch?v=0Oh_w5KrEVc
Professor Jan Blomgren: Så här uppstod elkrisen i Sverige
Nuclear can’t vary at all and must be used as a base load
Hydro can vary within a small window
DEMAND
SUPPLY
Must Balance
Watch this presentation

## Slide 17: Projected New energy split for 2050
Developed from a combination of an IRENA 2022 projection and some of my own assumptions
Global Wind & Solar capacity only (72.8%) = 26 220.7 TWh
4 weeks Wind & Solar capacity only = 2 017.0 TWh
This is the size of the needed power buffer
2nd generation of work done

## Slide 18: Number of technology units
Electric Vehicles
EV Batteries
Hydrogen fuel cells
Wind Turbines
Solar Panels
Power Storage Batteries

## Slide 19
(Source: The Role of Critical Minerals in Clean Energy Transitions IEA)

## Slide 20
Table A28. Metal required for stationary power storage batteries to phase out fossil fuels
2nd generation of work done
(Source: The Role of Critical Minerals in Clean Energy Transitions IEA)

## Slide 21: Metal produced in 2019
(Source: BGR 2021, USGS, Friedrichs 2022)

## Slide 22: Metal in 2022 global reserves
For every 1000 deposits discovered, 1 or 2 become mines
Time taken to develop a discovered deposit to a mine 20 years
For every 10 producing mines, 2 or 3 will lose money and shut down
Source: USGS

## Slide 23
Remember, this is for just the first generation of units. They will wear out in 10 to 25 years, after which they will need to be replaced
0.7% of passenger cars were EV in 2020
In 2018, renewables accounted for 4.05% of the global energy generation.
What is not constructed yet, cannot be recycled
The 1st generation at least must come from mining
If it was all constructed next year, it would not be until 2033 when large volumes would be available for recycling

## Slide 24: Conclusions
Current thinking has seriously underestimated the scale of the task ahead
Nuclear is vital to keep industry going but can’t be scaled up to be the only energy source
Biofuels may be the only way to power aviation and plastics. It cannot be scaled up to replace petroleum.
Battery chemistries other than lithium-ion should/will be developed, each with different mineral resources required
There is a projected mineral shortage to supply raw materials for battery manufacture
  2019 production rates are not even close to being appropriate
  2022 mineral reserves are also not large enough to deliver the needed volumes
Metals of all kinds are about to become much more valuable
  Evolution of the industrial ecosystem and its market is likely
There is a coming Renaissance for the exploration for and mining of minerals

## Slide 25
Simon P. Michaux
Associate Professor Geometallurgy
Unit Minerals Processing and Materials Research - Circular Economy Solutions
Ore Characterization, Process Engineering & Mineral Intelligence
Geological Survey of Finland/Geologian tutkimuskeskus
PO Box 96, (Vuorimiehentie 2)
F1-02151 Espoo, FINLAND
simon.michaux@gtk.fi
Mobile: +358 (0)50 348 6443
Kiitos
&
Thank you

## Slide 26: Metal Needed

## Slide 27: Stewardship of Planet Earth
An industrial ecosystem of unprecedented size and complexity, that took more than a century to build with the support of the highest calorifically dense source of cheap energy the world has ever known (oil) in abundant quantities, with easily available credit, and unlimited mineral resources
We now seek to build an even more complex system with very expensive energy, a fragile finance system saturated in debt, not enough minerals, with an unprecedented number of human population, embedded in a deteriorating environment.